## Slide 1
OLD HAM COUPLING MECHANISM
Presenting by:
David Ojha
Apar Jung Thapa
Sirish Shrestha
Presenting To:
Associate. Prof. Binaya Kc
TOM MINI PROJECT

## Slide 2
BACKGROUND
  It is used to connect two parallel shafts with slight lateral misalignment.
  Provides a constant 1:1 angular velocity ratio.
  Consists of two flanges and a floating intermediate disc.
  Commonly used where accurate power transmission is required.
Oldham's Coupling was invented by the Irish engineer John Oldham. It is a mechanical coupling used to connect two parallel shafts that have slight lateral misalignment while maintaining constant rotational speed.

## Slide 3
OBJECTIVES
  Study the working principle and kinematics of Oldham's Coupling.
  Design the geometry and dimensions of the coupling.
  Fabricate a functional prototype.
  Evaluate its ability to accommodate parallel shaft misalignment.

## Slide 4
APPLICATIONS
  CNC machines
  Servo motor and lead screw systems
  Robotic mechanisms
  Printing machines
  Textile machinery
  Precision measurement systems
  Rotary motion transmission in industrial equipment

## Slide 5
SCOPE AND LIMITATIONS
Scope
  Constant torque transmission.
  Handles slight parallel shaft misalignment.
  Compact, economical, and easy to maintain.
  Suitable for low to medium torque applications.
Limitations
  Cannot accommodate angular or axial misalignment.
  Sliding action causes wear and friction.
  Performance decreases at high rotational speeds.
  Prototype limited to functional demonstration only.

## Slide 6
COMPONENTS
1. Input Flange
  Mounted on the driving shaft.
  Transfers motion to the intermediate disc.
2. Intermediate Disc
  Floating member.
  Contains tongues on both sides placed at 90°.
  Slides inside the grooves of both flanges.
3. Output Flange
  Mounted on the driven shaft.
  Receives motion from the intermediate disc.

## Slide 7
WORKING PRINCIPLE
  Input shaft rotates.
  Input flange drives the floating disc.
  Floating disc slides inside the groove.
  Output flange receives motion.
  Output shaft rotates at the same speed.
  Sliding motion compensates for shaft misalignment.

## Slide 8
THEORITICAL FRAMEWORK
Oldham's coupling works based on kinematic principles.
It is considered an RP–PR mechanism, which is an inversion of the Elliptic Trammel mechanism.
Important Design Parameters
  Shaft offset distance
  Groove radius
  Radius of curvature
  Groove intersection angle (approximately 90°)
Mechanical Considerations
  Sliding motion causes friction.
  Larger groove radius reduces wear.
  Higher speed increases vibration and dynamic imbalance.
These parameters directly affect the efficiency and life of the coupling.

## Slide 9
DESIGN AND FABRICATION PROCESS

## Slide 10
ADVANTAGE
  Constant velocity transmission.
  Handles slight parallel misalignment.
  Compact design.
  Low manufacturing cost.
  Easy assembly.
  Easy maintenance.
  Smooth power transmission.
  Suitable for precision applications.
  Simple construction.

## Slide 11
CONCLUSION
The design and fabrication of the Oldham's Coupling successfully demonstrated constant velocity transmission between two parallel misaligned shafts. The prototype validated the working principle of the coupling and provided practical knowledge of mechanical design, fabrication, assembly, and testing, reinforcing the theoretical concepts learned in the Theory of Machines course.

## Slide 12
FUTURE WORKS
Future work can include high-speed performance testing, vibration and stress analysis using FEA, wear and fatigue evaluation, and testing under different loading conditions. Using improved materials or self-lubricating components can further enhance the coupling's durability and efficiency.

## Slide 13
THANK YOU!

## Slide 14
REFERENCES
  OLDHAM, J. – HISTORICAL DEVELOPMENT OF OLDHAM'S COUPLING.
  NORTON, R. L. DESIGN OF MACHINERY.
  SHIGLEY & MISCHKE. MECHANICAL ENGINEERING DESIGN.
  RATTAN, S. S. THEORY OF MACHINES.
  KHURMI & GUPTA. THEORY OF MACHINES.

## Slide 15
APPENDIX